## Slide 1
A data collection company utilizing vehicle mounted sensors
AutoSense
Analytics

## Slide 2
1
Lack of available data for Urban Infrastructure, needed for deployment and maintenance decisions
3
Not enough data for road quality and roughness, unsafe roads in need of maintenance
Network blind spots, weak signal strength, incorrectly positioned antennas
2
PROBLEM
STATEMENT

## Slide 3
AUTOSENSE ANALYTICS
Deploy sensors on moving vehicles to collect real-time mobile data across various routes
Adaptation of IoT Technologies
On-demand data collection
Centralized Data Integration Platform offering unified and complete data presentation and analysis
(B2B Company Model)

## Slide 4
Signal RSSI Mapping
4G (4G hat for Rpi)
LoRa (Arduino)
WiFi
  Detection of dead signal spots
  Creation of signal coverage heatmap
Measuring:
Providing:
  Information from the images collected and confirmation of data analysis results
Image Collection
Collecting:
Images from RPi camera
IMU Measurements
GPS position
Providing:
  Creation of road roughness heatmap, pointing the potholes
  Use photos for visual confirmation
Detecting:
Road roughness detection using IMU connected to RPi
Providing:
Road Roughness
COMPLETED PROJECTS

## Slide 5
FINAL ARCHITECTURE OVERVIEW

## Slide 6
HARDWARE AND SENSORS

## Slide 7
Hardware and Data Collection
  Connected via USB port to Rpi
  Retrives GPS and 4G RSSI values of NOVA Cellular Network (AT Commands) and posts it to FIWARE
GSM/4G LTE connection
  Enter APN for NOVA and start the data session
  Get the assigned IP address, gateway and DNS Servers
  Configure the Rpi Network Interface (assign the IP and set the default gateway) in order to route internet traffic through wwan0.
  Set Network Manager to manage the modem
  Create a saved 4G Connection
4G HAT

## Slide 8
IMU SENSOR
  Measuring the acceleration at x ,y ,z axis at a 20Hz rate
  Retrieving location, timestamp, speed, altitude from GPS Antenna every 2 seconds and posts it to FIWARE via 4G HAT, along with the accumulated acceleration measurements.
Data Processing
Data Collecting
  Keep only the z axis data, perform FFT for each window of 2 seconds (40 acc_z values)
  Pass through Filter and keep only the >5 Hz frequencies
  Calculate Roughness Score by summarizing the absolute values
  Edge Processing can be implemented

## Slide 9
CAMERA
Hardware and Data Collection
  Connected the camera via the Camera Serial Interface
  The IMU on the GPIO pins
  The 4G module, through USB
  Implemented threads to capture an image, collect 3-axis acceleration (IMU), GPS position (4G module) and post (HTTP) those to the Camera Controller via 4G.
Camera Controller
  Developed, containerize and hosted a Camera Controller
  Receives the image, extracts the metadata, stores the image and its corresponding data
  Provides an API, that offers access to the images

## Slide 10
LORA
  Using Arduino and Dragino for adding LoRaWAN connectivity
  A LoRa packet is sent from Dragino containing its current GPS location
  The LoRa antenna captures the LoRa signal and calculates the RSSI
  An MQTT notification is being published, containing GPS, Timestamp, LoRa RSSI
  Our backend controller has subscribed to the particular MQTT topic and posts the measurements to FIWARE
Utilized the work: https://github.com/Skorpinakos/LoRa-RSSI-Map

## Slide 11
REAL DATA COLLECTION AT CAMPUS AND CITY CENTER

## Slide 12
1
2
3
4
CHALLENGES
RSSI Heatmap Generation
IMU Data collection and processing
Combination of sensors (same interfaces)
Measurement interruptions due to shutdown or connection loss

## Slide 13
4G SIGNAL COVERAGE RESULTS
Patras City Center
University Campus
  Stronger RSSI at open space areas
  Weaker signal in the center due to buildings (shadowing, blocking)
  Dasilio Patras, despite the location of the antennas, weaker signal due to height differences (possible no LOS)
  Stronger 4G Signal at CEID (due to LOS)
  Weaker Signal between buildings (near BA weak)
Using NOVA Cellular Network

## Slide 14
ROAD DATA RESULTS
Confirmed by photos taken by Rpi Camera Hat
Road Roughness Heatmap
Road Roughness Score Points
Image Confirmation at GPS locations

## Slide 15
ROAD DATA RESULTS
Confirmed by photos taken by Rpi Camera Hat
Korinthou Road: Double-parked vehicles

## Slide 16
LORA SIGNAL COVERAGE RESULTS
  Stronger LoRa Signal at ECE Parking (IoT Sensors)
  Weaker Signal near Political Engineering Building

## Slide 17
1
2
3
LIVE DEMO
Simulation of 7 cars
Fake data generator, based on our real measurements
Parametric, customizable Dashboard and Live Map

## Slide 18
WEBSITE: STRUCTURE AND FEATURES
1
Company Website (publicly accessed)
  Info/Contact etc.
  Login/Register
2
Admin Portal
  Manage users and projects
  Monitor Live Status
  Access to all projects
3
Client Portal
  Monitor the projects they are enrolled
  Customizable Preferences (Light/Dark theme)
4
Dashboards and Heatmaps
  Custom Dashboards and Heatmaps are embedded on the website page of the corresponding project
5
API
  API implementation and documentation for each project
  Easily accessible data (JSON Format)
http://labserver.sense-campus.gr:7101/

## Slide 19
USER PAGES

## Slide 20
ADMIN PAGES

## Slide 21
API

## Slide 22
IMU
ACC
Backend Controller
(Hosted on Lab Server)
LIVE DEMO
Lab Server: 3306
Lab Server: 7101
Lab Server:8086
Lab Server: 1026
Lab Server:8087
Our Website

## Slide 23
TASK DISTRIBUTION
  IoT Agent and FIWARE communication
  Retrieving GPS coordinates from modules and combine them with RSSI values
  LoRa, Camera, WiFi configuration
  IMU and edge processing using fft, bandpass filters
  4G measurements and utilization of hat as a modem
  Combination of sensors and communication using Threads
  Containerization of Website, Controllers and host them on lab server using Docker
  Local Data Base Storage on RPi
  Back-end controller syncing data between InfluxDB and FIWARE’s MySQL DB
  FIWARE notifications to Back-end Controller
  Camera Controller
  Data analysis and representation (e.g. heatmaps)
  Grafana Dashboards and InfluxDB
  Live Demo using Real Data
  Web Development: Front-End, Back-End
Real Time Measurements

## Slide 24
OUR PROJECT AVAILABLE ON
GitHub
(Source Code)
YouTube (Video Demo)
Website

## Slide 25
OUR TEAM
Georgios
Stergiopoulos
+30 6931152410
gstergiopoulos@ac.upatras.gr
Student @ ECE Upatras
Specialization
Computer Engineering
Eleni Sakellariou Matsi
+30 6987095462
up1084047@ac.upatras.gr
Student @ ECE Upatras
Specialization
Communications

## Slide 26
Connect with us.
Thank's For Watching
AutoSense
contact@autosense.com
+30-2610-995-386
Analytics